Coherent Beacon Data, Wallops Island Receiver
Robert Livingston, Scion Associates, Inc.
Terry Bullett, NOAA NGDC

---
Coherent Beacon System
high dynamic range complex signal scintillation receiver that also provides direct total electron content measurement.
three channel receiver system
  - analog down conversion to intermediate frequencies of 15, 40 and 106.7 MHz
  - analog dynamic range > 80 dB
  - integral multiply phase lock oscillators
  - loop bandwidths optimized for minimum phase noise
  - geometrical/dispersive phase separation (in software) as in traditional hard-limiting coherent beacon receivers
digital down conversion to baseband
  - open-loop data collection in bandwidths that accommodate geometrical Dopplers
  - 104 dB digital dynamic range
  - raw I/Q data collected for post-processing
  - post-processing SNR gains of 30 dB can be achieved

---
Overall Intensity/Doppler Data
[Speaker Notes: The top frame shows signals strengths throughout the flight (separated by 10 db for clarity). The two rocket burns are conspicuous in the data, indicating that the ray path was near or within the wakes. The bottom frame shows the measured 150 MHz and 400 MHz Doppler tracks, along with that for the NASA predicted trajectory. Looking nearly up along the flight trajectory, the Doppler reversals are very fast. In the figure, four portions of the track are indicated, (I) spin-up, (II) third stage burn, (III) curiosities, and (IV) fourth stage burn. These are looked at more closely in the following slides.]

---
Overall Intensity/Dispersive Phase (TEC) Data
[Speaker Notes: The top frame signal intensity for the two beacons, and is the same as in the previous figure. The lower frame shows the 150 MHz dispersive phase (i.e. delta-TEC) that remains after direct removal of the geometrical Doppler (subtraction of the ratio-scaled measured 400 MHz phase from the 150 MHz measured phase). The observed peak of approximately 38 TEC units should be compared with that from other beacon receivers that were operating.]

---
Spin-Up Period
[Speaker Notes: For approximatey the first 10 seconds after launch, both the 150 MHz and 400 MHz signals saturated the receiver converter, as is indicated. The derived phase ia not affected by the saturation. The jump in signal levels at ~23:46:20 are probably attributable to re-orientation of the antenna on the beacon after the maneuver. The measured Doppler shifts match that of the specified trajectory well, including the spin-up.]

---
Third Stage Burn Period
[Speaker Notes: The spin of the rocket is clear in both the signal intensities. The burn produces both a fade in the signals, and some degree of scattering or structure. The acceleration during the burn must be relatively gradual, with the Doppler changing only near the end of the burn period.]

---
Third Stage Burn Scattering/Structure
[Speaker Notes: The two top frames show the 150 MHz structure during the third stage burn after (1) removal of the ~5 Hz spin, and (2) filter detrending. The power spectrum of the phase structure is shown in the lower frame. If there are convective irregularities in the engine plasma wake, a phase-screen approach would show a power-law slope in the spectrum, as this one does.]

---
Curiosity Period
[Speaker Notes: These frames start just as the beacon is entering the lower F layer. The change in 400 MHz signal strength at 23:47:37 is followed by several slow fades, and corresponds to a change in the spin characteristic of the 150 MHz signals. There is no dispersive phase variation during this period so perhaps this is related to the beacon antenna being in the plasma, the fades being multipath from the rocket body.]

---
Fourth Stage Burn Period
[Speaker Notes: The fourth stage burn produces a very rapid attenuation in the 150 MHz signal, which ends just as rapidly at the end of the burn. The 400 MHz signal is affected much less, mostly showing some enhancement of the spin pattern. The cause of the rapid drop in 400 MHz signal at 23:52:37 (well after the burn) is unknown. The acceleration during this burn was much less gradual than with the third stage, with an obvious rapid response in the Doppler shift. Although the burn timing seems exact, deviation in the Doppler indicates a change from the nominal payload trajectory.]

---
Fourth Stage Burn Scattering
[Speaker Notes: The two top frames show the 150 MHz structure during the fourth stage burn after the same spin removal and filter detrending as the third stage burn figure. In the lower frame, the power spectrum of the 150 MHz phase structure is very different than that of the third stage burn. The scattering is stronger, and the spectrum is broad and flat spectrum at intermediate frequencies. The flat spectrum suggests scattering from dense debris in the absence of plasma irregularities. However, the much weaker scatter at 400 MHz, and the more effective extinction of the 150 MHz signal are inconsistent with this idea. Perhaps severe coning effectively separated the transmission paths relative to the debris burst.]